## Slide 1: JLEIC Design Update (Oct. 2018)
JLEIC Collaboration

## Slide 2: EIC Performance Requirements: NAS report
√sep range ~20 to ~100 GeV upgradable to ~140 GeV
Ion beams from D to heaviest stable nuclei
100 to 1000 times HERA luminosity—will discuss what this means
At least ~70% polarization for electrons, protons and light ions
One or more IR with integrated detector with high acceptance

## Slide 3: JLEIC Design Update (Oct. 2018)
arXiv:1504.07961
2015
2017
2018
Update History
Document
Under development
This Update
Fundamental concept unchanged
This update:
Increase √s range by increasing ion ring dipoles from 3T6T.
Keep the land footprint of the design the same.
The luminosity performance satisfies the requirements.
IR design retains high acceptance.
Polarization remains high.
Relatively small design changes

## Slide 4: JLEIC Design Update (Oct. 2018)
beam energy range:
Ee: 3 to 12 GeV (same as before)
Ep: 30 to 200 GeV (enabled by 3T6T dipoles) upgradable to 400 GeV (use HE-LHC/FCC development—12T dipoles)
Electron complex (unchanged)
  CEBAF
  Electron collider ring
Ion complex (mainly incremental changes)
  Ion source
  SRF linac
  Booster
  Ion collider ring (3T6T dipoles)
Fully integrated high-acceptance IR (being re-optimized for higher energies) and detector
  2 IRs with same acceptance
DC and bunched beam coolers (incremental changes + no BBC concept)
JLEIC Energy: √s = 20 to 100 GeV upgradable to 140 GeV
✔
Most of the design remains the same
✔

## Slide 5: High luminosity: multi-phased cooling
ion sources
ion linac
Booster
(0.285 to 11 GeV)
collider ring
(11 to 200 GeV)
BB/DC cooler
DC cooler
DC cooling for emittance reduction
BBC cooling for emittance preservation against intra-beam scattering
4.3 MeV DC Cooler @Fermilab
Ring | Functions | Kinetic energy (GeV / MeV) |  |  | Cooler type
 |  | Proton | Lead ion | Electron | 
booster ring | Accumulation of positive ions |  | 0.1 (injection) | 0.054 | DC
collider ring | Maintain emitt. during stacking | 11 (injection) | 3 (injection) | 6.0 (proton) 1.6 (lead) | DC
 | Pre-cooling for emitt. reduction | 11 (injection) | 11 (ramp to) | 6.0 | DC
 | Maintain emitt. during collision | Up to 200 | Up to 78.3 | Up to 109 | BBC/ERL

## Slide 6: Bunched Beam Cooling
Enabling technologies :
Fast kickers, risetime <1 nsec
Magnetized source ~75mA
ERL cooler +
Multi-turn circulator ring

## Slide 7: High polarization: Figure-8
Figure-8 concept: spin precession in one arc is exactly cancelled in the other
Spin stabilization by small fields: ~3 Tm vs. ~ 400 Tm for deuterons at 100 GeV
  Criterion: induced spin rotation >> spin rotation due to orbit errors
Highly polarized deuteron beams will run in JLEIC
3D spin rotator: combination of small rotations about different axes provides any polarization orientation at any point in the collider ring
No effect on the orbit
Adiabatic spin flips
Spin tracking in progress
IP
Spin Rotator
e-
Magnetic field
Polarization
E- energy (GeV) | 3 | 5 | 7 | 9 | 10
Estimated Pol. Lifetime (hours) | 66 | 5.2 | 2.2 | 1.3 | 0.8
Electron polarization
n = 0
Ion polarization
Polarization for proton, light ions (incl. deuterons), electrons >80%.
✔

## Slide 8: Luminosity Discussion
In HERA-2, ~600 pb-1 of integrated luminosity
was delivered (to ZEUS) over ~1000 days of
running.
The means that HERA-2 delivered
~0.6 pb-1/day or ~4 pb-1/week of integrated
luminosity during “running”. There were two collider
experiments, so inflate this a little to 6 pb-1/week
6 pb-1/(one week in seconds) = 1031 cm-2s -1
This is the average luminosity of HERA while running
We would like to have 100 – 1000 times HERA luminosity:
So the aim for the EIC is 0.6 fb-1 to 6 fb-1/week of running.
Or average luminosity (while running) of 1033 to 1034 cm-2 s-1
6 fb-1/wk  100 fb-1/yr assuming 107 s in year (running ~1/3 of the year
or a “snowmass” year)
average while running (not instant, not peak, etc.)
Average luminosity (while running) is quoted for JLEIC

## Slide 9: JLEIC Average Luminosity and Energy Reach
Average luminosity during running (operational inefficiency taken into account): i.e.
Integrated luminosity = Av. Lumi × Time of running
Luminosity 100 to 1000 time that of HERA over the energy range
✔
Note good perf. w DC only

## Slide 10: JLEIC Luminosity and Energy Reach with Upgrade
Note: Total of ~640 fb-1
  1034 cm-2s-1  6 fb-1/week,
  ( >100 fb-1 /year)
  1033 cm-2s-1  0.6 fb-1/week,
  ( >10 fb-1 /year)
Average luminosity during operation: i.e.
Integrated luminosity = Av. Lumi × Time

## Slide 11: JLEIC SUMMARY
The basis of the design (ring-ring, high luminosity by high rep-rate, high polarization with Figure-8, full event coverage, and minimization of technical risk) has remained constant since 2005
The energy reach is √s =20 to 100 GeV upgradable to 140 GeV, using 12 T magnet technology being developed for CERN projects HE-LHC and FCC.
The design delivers average luminosity of 1033-34 cm-2 sec-1 in the almost the entire energy range with only DC cooling.
The figure-8 design achieves >80% polarization for both light ions (including deuteron) and electrons.
A pre-CDR with a full description is under preparation. There may be a minor update to the parameters upon its release.
The overall design risk is low in most areas.
Technology demonstration is needed primarily for the bunched beam electron cooling; However, very good performance can be achieved with only DC cooling.
✔
✔
✔