## Slide 1: Observation of Nonstandard Radioxenons
Michael Mayer
ODU Nuclear Seminar Talk
PNNL-SA-188612
Notes: Stock image of cloud formations

## Slide 2: Atmospheric Monitoring for Nuclear Explosions
Radioactive xenon isotopes are monitored around the world for nuclear explosion monitoring
  International treaty verification
  Background monitoring
  Nuclear disaster observations

## Slide 3: Atmospheric Xenon Sampling
Traditional backgrounds of atmospheric xenon samplers
  Medical isotope production facilities
  Nuclear reactors
  No others observed until now
Conventional radioxenons observed
  135Xe, 133Xe, 131mXe, and 133mXe
  Typically observed with electron-photon (beta-gamma) coincidence detectors on an atmospheric radioxenon system

## Slide 4: Radioxenon Backgrounds

## Slide 5: Radioxenon Monitoring Systems
Four technologies for monitoring radioxenon
  ARSA - β-γ-coincidence
  SAUNA - β-γ-coincidence
  SPALAX – High-res γ
  ARIX - β-γ-coincidence
One to two samples a day
  12-hr to 24-hr collection times
Sensitivities for 133Xe around 0.2-0.6 mBq/m3
Uncoated cells have memory effect
ARSA SAUNA
SPALAX ARIX

## Slide 6: Radioxenon Detection
Xenon coincidence decays
  beta and gamma
  conversion electron and X-ray
Plastic scintillator to detect the betas and conversion electrons
NaI(Tl) to detect the gammas and X-rays

## Slide 7: Beta-Gamma Coincidence Measurements
Typical beta-gamma histogram
Ephoton
Ebeta
133gXe
131mXe 133mXe
135gXe
Typical background suppression
  Gamma singles (top)
  Beta-gated Gamma (bottom)

## Slide 8: 7 Regions of Interest (US Method)
Regions used to determine number of “counts” or decays detected
Regions used to identify largest decay signatures of a specific isotope
Seventh region used to remove Xe-131m and Xe-133m from Xe-133
  The 30-keV region of 133Xe contains 131mXe and 133mXe

## Slide 9: Example Spectra
Background 222Rn (214Bi and 214Pb)

## Slide 10: Example Spectra
135Xe 131mXe

## Slide 11: Example Spectra
133Xe 133mXe (133Xe)

## Slide 12: Xenon International
Next generation atmospheric radioxenon system
Developed at PNNL
  Transitioned to Teledyne Brown Engineering for production (Knoxville, TN)
Faster and more sensitive than current certified systems
  ~2.5 cc of xenon in 6 hours
  Compared to ~1 cc for SAUNA
Minimum Detectable Concentrations
  <0.15 mBq/SCM for 133Xe, 131mXe, 133mXe
  <0.5 mBq/SCM for 135Xe

## Slide 13: Xenon International
Next generation atmospheric radioxenon system
Developed at PNNL
  Transitioned to Teledyne Brown Engineering for production (Knoxville, TN)
Faster and more sensitive than current certified systems
  ~2.5 cc of xenon in 6 hours
  Compared to ~1 cc for SAUNA
Minimum Detectable Concentrations
  <0.15 mBq/SCM for 133Xe, 131mXe, 133mXe
  <0.5 mBq/SCM for 135Xe

## Slide 14: Testing at TBE in Knoxville, TN
Four detectors running consecutively
  Average ~2.5 cc per run
Nothing anomalous noticed
  Run sample measurements were good
  System during the time frame was good

## Slide 15: Puzzling Observations and Analyses
At initial glance, everything seems to be going well
  133Xe – no unusual levels observed for the area
  135Xe – high but also not too unusual for the area
  133mXe – unusual to have higher than concentration than 133Xe
  131mXe similar to 133mXe
Further investigation showed that the gamma-ray spectrum has unusual features.
133mXe
133Xe

## Slide 16: Puzzling Observations and Analyses
At initial glance, everything seems to be going well.
  133Xe – no unusual levels observed for the area
  135Xe – high but also not too unusual for the area
  133mXe – unusual to have higher than concentration than 133Xe
  131mXe similar to 133mXe
Further investigation showed that the gamma-ray spectrum has unusual features.
  Does not look like traditional Xe or Rn daughters
Gamma Singles Spectrum

## Slide 17: Atypical Coincidence Signatures

## Slide 18: Isotope Identification
Assuming system working optimally
  Only Xe in system
Possible Xe isotopes observed experimentally previously
  127Xe and 125Xe
  Produced via neutron irradiation
125Xe, 127Xe, and 129mXe all identified in data sets
122Xe originally disregarded as candidate due to only being produced as medical isotope via proton or alpha bombardment
McIntyre, Justin I et al.. 2008. “Generation of Radioxenon Isotopes.” In Proceedings of the 30th Seismic Research Review: Ground Based Nuclear Explosion Monitoring Technologies, 793–801.

## Slide 19: Monte Carlo Simulations
Monte Carlo simulations performed to observe clean signatures and extract efficiencies
Region at 511 keV in gamma energy not identified with simulations
127Xe Simulation
129mXe Simulation
125Xe Simulation
Xenon International Measurement

## Slide 20: Missing Piece
122Xe did not originally seem to produce missing signature
  Including daughter 122I (T1/2=3.63 minutes) produces missing signature
Production does occur via spallation in the mercury target at SNS
122Xe Only Simulation
122Xe Full Decay Chain Simulation

## Slide 21: How much did we see? Xe-122 Concentration Analysis
The concentration can be calculated using the Bateman equations
  Relates number of counts of 122I to starting amount of 122Xe
  Assumed no memory effect (coated cells)
Decay corrected to account for collection and processing time
  Acquisition decay accounted for with Bateman equation
MDC can be formulated using the standard equations
Efficiency values obtained from simulation
*

## Slide 22: Concentration of 122Xe over Sampling Period

## Slide 23: Atmospheric Transport Modeling
Modeling suggests that likely release is from HFIR or SNS
Wind patterns are not consistent with release from the nuclear power plants
Production mechanism suggests
  SNS only
  SNS and HFIR
Publication on ATM
Eslinger, Paul W. et al. 2022. “Determining the Source of Unusual Xenon Isotopes in Samples.” Journal of Environmental Radioactivity 247 (June): 106853. https://doi.org/10.1016/J.JENVRAD.2022.106853.

## Slide 24: 122Xe Concentration: Schedule Overlayed/Zoomed
*No operational dates prior to the first SNS outage

## Slide 25: Conclusion and Outlook
Newly observed isotopes seen near HFIR and SNS suggest new source of interfering xenon background (scientific research facilities)
  Neutron irradiation and spallation facilities can produce and release xenon
  Several online or coming online:
    ISIS neutron source in the UK,
    Japan Proton Accelerator Research Complex (J-PARC) in Japan,
    Los Alamos Neutron Science Center (LANSCE) and SNS in the USA,
    European Spallation Source in Sweden, and the
    China Spallation Neutron Source
New isotopes interfere with all traditional ROIs used for activity calculations
  Algorithms will continue to calculate normally
  Concentrations and ratios will not make sense
Preliminary work completed identifying source(s) and quantifying
  Concentration values have been calculated for 122Xe
  Work needs to be done to determine observation elsewhere and impact